## Slide 1: Report: an evaluation of the risk of airborne transmission of COVID-19 on the 802 train carriage
TRACK WP5
Huw Woodward, Rick de Kreij, Laetitia Mottet, Emily Kruger, Sarkawt Hama, Arvind Tiwari, Prashant Kumar,
Christopher Pain, Paul Linden
1

## Slide 2
Report objectives
What is our best estimate of the risk of infection via the airborne route?
What is the infection rate integrated over all passengers?
To what extent does this risk depend on the location of the infected person and other passengers?
Is the well-mixed assumption suitable to estimate the risk of airborne transmission?
2

## Slide 3
Conducted experiments
CO2 measurements for a controlled experiment during Autumn 2020
In-service CO2 measurements taken in November 2020 over the course of 2 days
Measurements of the concentrations of salt aerosol droplets released from a nebuliser during February 2021
HVAC filter efficiency tests
1
3
4
2
3

## Slide 4
Modelling
CFD simulation of controlled CO2 experiments
1D diffusion-advection contaminant model
1
2
4

## Slide 5
Risk and secondary infections estimates from CO2
In service estimation:
Viral load will vary per person
Quanta released depends on activity level
 |  | 1 infected in carriage |  | Prevalence of virus 1/500 | 
136 passengers 2600 ppm | Individual infection risk | 0.043 % | 4.17 % | 0.012 % | 1.12 %
 | Secondary infections | 0.058 | 5.63 | 0.016 | 1.51
 |  | 1 infected in carriage |  | Prevalence of virus 1/500 | 
 | Individual infection risk | 0.043 % | 4.17 % | 0.012 % | 1.12 %
 | Secondary infections | 0.058 | 5.63 | 0.016 | 1.51
Individual infection risk from CO2:
with
5

## Slide 6
Source location | Centre | Average of all locations | End
Difference | + 28 % | 0 | - 49 %
Ventilation rate | No ventilation | Operational | Maximum
Difference | + 229 % | 0 | - 51 %
Physical distancing | 0 rows | 1 row | 2 rows | 3 rows
Difference | 0 | - 6 % | - 14 % | - 22 %
Journey duration | ½ hour | 1 hour | 2 hours
Difference | - 58 % | 0 | + 117 %
Filtration | No filtration | 1 filter (10%) | 2 filters (20%) | Full removal (100%)
Difference | 0 | - 13 % | - 23 % | - 61 %
Infection risk dependence
Average risk of 1D model for an unknown source location equals risk of fully mixed model
Except when physical distancing is included
Quanta | 1 | 100
Difference | 0 | + 9731 %
Quanta |  | 
Difference | 0 | + 9731 %
Individual infection risk:
Individual infection risk is estimated with fully mixed and 1D model
Base configuration “0”: infection probability 0.056 %
6

## Slide 7
Concerns HVAC design and possible workaround
 | Fresh air supply
Design specification | 20 – 26.7
In service CO2 measurements | 9.9 – 10.8
CFD controlled CO2 | < 14
1D-model controlled CO2 | 11.4
CO2 decay curves | 10.7
Design specification | 20 – 26.7
In service CO2 measurements | 9.9 – 10.8
CFD controlled CO2 | < 14
1D-model controlled CO2 | 11.4
CO2 decay curves | 10.7
Estimated fresh air supply is much lower compared to design specifications
Likely to be induced by leakage into the vestibule and/or decrease decreases
Workaround: keep door to vestibule open increases increases
7
FRESH-AIR

## Slide 8
A methodology for evaluating the effective ventilation rate within public transport vehicles
Estimate ventilation rate from CO2 decay
Stage 1: decay of peak
Stage 2: decay of mixed carriage
Estimated ventilation rate 802 carriage: 10.7
Improve method:
More sensors
Higher concentrations
Longer measurement duration
Measurements conducted by
Jonathan Bridgewood - Group Rail Technical Director
8

## Slide 9: Laboratory Experiments
Heated Pipe
Tank Inflow
Tank Outflow
Waste
F
F
Fresh In
F
Flow meter
Thermocouple
Inflow
Outflow
Inflow
Outflow
20cm
50cm
15cm

## Slide 10: Scalings
Volume Fluxes per unit length:
Momentum Flux per unit length from top:
Buoyancy Flux per unit length from bottom:
Jet Length:
Mixed Flow:
Stratified Flow:
Heated Pipe
L
H

## Slide 11: Example Experiments

## Slide 12: Example Temperature Measurements

## Slide 13
Limitations and future work
Lack of experimental or CFD analysis for a carriage with high occupancy
1D model assumes well mixed across its cross-section (might change with heating and/or high occupancy)
Awaiting results of nebuliser measurements February
Quantify the effect of opening/closing doors
Estimate HVAC filtration efficiency
Estimate infection risk in both longitudinal and lateral directions
Verify zonal model (extension of 1D advection-diffusion model)
13